Cisco Systems, Inc.

Firmware File Version 3.0.033

June 2007

Copyright (C) 1999-2008 Cisco Systems, Inc. All rights reserved. Printed in the

USA. Cisco, Cisco Systems, and the Cisco Systems logo are registered trademarks

of Cisco Systems, Inc. in the U.S. and certain other countries. All other

trademarks mentioned in this document are the property of their registered

Owners .

=========================================================================

Table of Contents

=========================================================================

1. Firmware file details and purpose

2. Target Platforms

3. Instructions for upgrading the firmware file

4. Caveats

=========================================================================

1. Firmware file details and purpose

The Firmware file version (3.0.033) resolves some of the specific ADSL interoperability issues (Refer to Caveats). The firmware is compatible with IOS release 12.4(6)T and later and 12.4(11)XJ. The firmware 3.0.33 has been certified by specific carriers and should not be used for general deployment.

Refer individual platform data sheets for complete DSLAM interoperability details

2. Target Platforms

Loading of the firmware file from flash separate from IOS is supported on all the Fixed ADSL Integrated Services Routers as well as the ADSL HWIC. Following is the list of platforms supported:

1 .Cisco 857

2. Cisco 876, Cisco 877

3. Cisco 1801, Cisco 1802

4. HWIC-1ADSL1, HWIC-1ADSLI, HWIC-ADSL-B/ST, HWIC-ADSLI-B/ST

5. Cisco 1801-M, and Cisco 877-M

3. Instructions for upgrading the firmware file

1. Download the file and rename the file "adsl_alc_20190.bin".

2. Copy the firmware file to the flash:

3. For the new firmware to take effect, reboot the device.

4. The “show dsl interface atm 0” output gives the details of the firmware file in use

Snapshot example taken from the output of  “Show dsl interface atm 0” command

| Firmware file in flash is used | Firmware file embedded in IOS is used |
| --- | --- |
| Init FW: init_AMR-3.0.033.bin Operation FW: AMR-3.0.033.bin FW Version: 3.0.033 | Init FW: embedded Operation FW: embedded FW Version: 2.5.42 |

Note:

- The firmware file should not be renamed when being copied  to the flash , Since the router looks for the presence of file named "adsl_alc_20190.bin" to initiate the flash upgrade process

- If IOS is now able to find a valid firmware in the flash then it would always use that rather than the firmware embedded in IOS. If users want to use the embedded firmware, they have to ensure that there is no valid firmware file in flash.

4. Caveats

The following issues are fixed in the latest firmware 3.0.033 since 3.0.14 -

CSCsf11228: 85x/87x/180x ping delay is higher, than with an external modem

CSCse94912: 1801 does not train at ADSL2+ rates to Alcatel 7302